## Slide 1: Makefile Course

## Slide 2: Mục tiêu khóa học
Nắm được Build Process cơ bản trong hệ thống nhúng
Biết cách sử dụng Compiler GCC
Nắm bắt được các khái niệm cơ bản về Makefile
Cách viết Makefile cho một project Vi điều khiển
Tổng quát hóa Makefile cho các project khác nhau

## Slide 3: Giới thiệu
Tác giả: Nguyễn Văn Nghĩa
  SĐT/Zalo: 0986.951.957
  Facebook:
    Cá nhân: https://www.facebook.com/nghia12a1
    Nhóm: https://www.facebook.com/groups/laptrinhdientu
  Blog: https://laptrinhcnhung.blogspot.com/
Tham khảo:
  Tài liệu Makefile GNU
Slide giữ các từ khóa/mô tả bằng tiếng anh

## Slide 4: Nội dung
Build Process
GCC – Command Line
Makefile Vi điều khiển
Tổng quát hóa Makefile
Chương trình Makefile đơn giản
1
2
3
4
5

## Slide 5: Build Process
Từ Source Code đến file nhị phân nạp vào Target

## Slide 6: Build Process – Basic
preprocessor
Compilation
Assemble
Linking
Source files (.c / .cpp / .h)
Include Header/ Expand Marco (.i / .ii)
Assembly Code (.s)
Object File (.o)
Executable file (.exe)
Source files (.s)
Static Library (.lib / .a)

## Slide 7: Build Process – Embedded
preprocessor
.c .cpp .h
Object files
parser
Code generator
Assembler
.i
.s
.o
Processor architecture specific machine codes with no absolute address (relocatable file)
Extended files
Assembly files
Source files

## Slide 8: Build Process – Embedded
Linker
.o
Re-locatable object files
.a
Static Libraries
.elf
Executable & debug file
Objcopy tool
.ihex
.bin
Intel hex format
Bin format
Locator
Linker script
.ld

## Slide 9: Đọc thêm
Preprocessor https://laptrinhcnhung.blogspot.com/2021/08/Preprocessor.html
Build Process https://laptrinhcnhung.blogspot.com/2021/08/Build.html
Cross Compiler https://laptrinhcnhung.blogspot.com/2021/08/CrossCompiler.html
Quá trình Linking https://laptrinhcnhung.blogspot.com/2021/08/Linking.html
Static Library vs Shared Library https://laptrinhcnhung.blogspot.com/2021/08/Library.html
Linker Script File https://laptrinhcnhung.blogspot.com/2021/08/LinkerScriptFile.html

## Slide 10: GCC – Command Line
Giới thiệu trình biên dịch GCC
Command Line cơ bản và sử dụng GCC với Build Process
Makefile - Lí do cần sử dụng Makefile

## Slide 11: Trình biên dịch là gì?
“Compiler (trình biên dịch) là một chương trình máy tính làm công việc dịch các chuỗi câu lệnh viết bằng ngôn ngữ lập trình thành chương trình tương đương nhưng viết dưới dạng ngôn ngữ máy tính. Chương trình mới này được gọi là mã đối tượng (object code)”.

## Slide 12: GCC là gì?
GCC - GNU Compiler Collection - tập hợp các trình biên dịch được thiết kế cho nhiều ngôn ngữ lập trình khác nhau
Thành phần quan trọng của GNU toolchain
Compilation
Assemble
Include Header/ Expand Marco (.i / .ii)
Assembly Code (.s)
Object File (.o)
Source files (.s)

## Slide 13: Cài đặt GCC
GCC có sẵn khi cài CodeBlock/Dev C++
GCC – MingW https://codecute.com/c/huong-dan-cai-dat-trinh-bien-dich-c-c-mingw-gcc.html
GCC – Cygwin https://codecute.com/c/cygwin-la-gi-cai-dat-compiler-c-c-cygwin-tren-windows.html

## Slide 14: Command Line
Kiểm tra GCC version
Tạo folder mới
Tạo một file source
Tạo một file mới

## Slide 15: Command Line
Preprocessor
Compilation
Assemble
Linking

## Slide 16: Command Line
preprocessor
Compilation
Assemble
Linking
Source files (.c / .cpp / .h)
Include Header/ Expand Marco (.i / .ii)
Assembly Code (.s)
Object File (.o)
Executable file (.exe)
Source files (.s)
Static Library (.lib / .a)

## Slide 17: Chương trình Makefile đơn giản
Tại sao cần sử dụng Makefile
Khái niệm cơ bản trong Makefile
Viết Chương trình Makefile đơn giản với C

## Slide 19: Why you need makefile?
Add this file to the project & Rebuild all file
Your project have many source files and you build it by an IDE (Keil C)
At a time, you want to edit or add a file
It spend many time to rebuild with a big project
You just need to build edited/added files: led .c
Makefile???
Build only

## Slide 20: What is Makefile?
Makefile is a script file format that contains some information:
  Project structure (file, dependencies)
  Commands to create files (object file, elf/bin/hex files, …)
  The make command will read makefile content, understand project’s structure and execute the commands
Tools for Makefile:
  Cygwin/Mingw/GNU Make

## Slide 21: From GCC commands to Makefile
My project:
main.c  main.o  main.exe
With GCC:
With Makefile:
main.c
Generate object file
Generate .exe file
Run .exe file
Results
Combine GCC commands into one script file

## Slide 22: Cài đặt Cygwin
https://www.cygwin.com/ Đã cài đặt ở bài số 2 – Lưu ý, cài đặt packgage GCC và make

## Slide 23: Rules Makefile
Basic form of a basic simple makefile
Tab space
Action that make carry out
Input files to make target
Action / File target

## Slide 24: For examples
Target file
Actions
Input files to make target file
Input files to make actions
Action that make carry out

## Slide 25: Một số khái niệm cơ bản trong Makefile

## Slide 26: PHONY keyword
I have a file has the same name with an action
Action ‘build’ is not running with make command
Add PHONY keyword to signal ‘build’ is a action

## Slide 27: Variables in Makefile
Variable names
Values
Assign symbols
Symbol to access the value of a variable: $(variable_name)
Use to generalize makefile, avoid using specific names of files

## Slide 28: Print value of variables
Printing value of variables to check, debugger when working with makefile  Use ‘echo’ command & string substitution
Results

## Slide 29: Tài liệu makefile
Tài liệu https://www.gnu.org/software/make/manual/make.html

## Slide 30: Chương trình Makefile - Vi điều khiển
Makefile với Vi điều khiển
Thực hành viết Makefile với Chương trình Vi điều khiển

## Slide 31: Cài đặt Phần mềm
Toolchain – GCC for ARM https://developer.arm.com/tools-and-software/open-source-software/developer-tools/gnu-toolchain/gnu-rm/downloads
Phần mềm nạp code STM32 ST-LINK Utility https://www.st.com/en/development-tools/stsw-link004.html
Tài liệu https://www.gnu.org/software/make/manual/make.html
Source Code https://github.com/nghia12a1-t-ara/makefile

## Slide 32: Bài toán
Viết Makefile cho Chương trình Vi điều khiển sau:
  Blink LED GPIO
    Source Code (GPIO.c / GPIO.h / main.c)
    Startup File, Linker File – Được cung cấp
  Phần mềm hỗ trợ nạp code
    STM32 ST-LINK Utility
  Phần cứng: STM32 (Mình sử dụng STM32F401 – NUCLEO Board)

## Slide 33: Build Process
preprocessor
.c .cpp .h
Object files
parser
Code generator
Assembler
.i
.s
.o
Processor architecture specific machine codes with no absolute address (relocatable file)
Extended files
Assembly files
Source files

## Slide 34: Build Process  Bài toán
main.c
GPIO.h
GPIO.c
main.i
GPIO.i
main.s
GPIO.s
startup.s
main.o
GPIO.o
startup.o

## Slide 35: Build Process
Linker
.o
Re-locatable object files
.a
Static Libraries
.elf
Executable & debug file
Objcopy tool
.ihex
.bin
Intel hex format
Bin format
Locator
Linker script
.ld

## Slide 36: Build Process  Bài toán
main.o
GPIO.o
startup.o
Linker
Locator
stm_ld.ld
Objcopy tool
GPIO.elf
GPIO.hex
GPIO.bin

## Slide 37: Command
Compile / Linker <Compiler Options> -o <Target> <All Prerequisite> < Linker Options> -o <Target> <All Prerequisite>
Create hex, bin, elf for Microcontrollers Linker  file elf < Linker Options> -o <Target> <All Prerequisite>
Object Copy to Create hex file objcopy.exe -O ihex <file elf> <file hex>
Nạp code ST-LINK_CLI.exe –ME ST-LINK_CLI.exe -p <file hex> <Địa chỉ bắt đầu nạp code> ST-LINK_CLI.exe -rst

## Slide 38: Compiler Options
arm-none-eabi-gcc
-mcpu=cortex-m4
-mthumb
-std=gnu11
-Ox
-I$(Include_DIR)
Linker Options
arm-none-eabi-ld
-T $(LINKER_FILE)
-Map <path_to_file.map> -Wl,-Map= <path_to_file.map>
-nostdlib

## Slide 39: Tổng quát hóa Makefile
Các từ khóa/function trong makefile
Thực hành tổng quát hóa Makefile với bài toán VĐK

## Slide 40: Automatic Variables
Symbols | Meaning
$@ | File name of the target of the rule
$^ | Name of all the prerequisite
$< | Name of the first prerequisite
Some symbols used to generalize the rules

## Slide 41: ‘wildcard’ Characters
The wildcard characters in make are ‘*’, ‘?’, ‘[…]’
For examples, *.c specifies a list of all the files whose names end in ‘.c’
Clear all files in ‘output’ folder
Get all files in the PATH C:\Users\Admin\...

## Slide 42: ‘foreach’ function
This function causes one piece of text to be used repeatedly, each time with a different substitution performed on it.
Get all files in the all folder of dirs.

## Slide 43: Make Process
GPIO.hex
GPIO.elf
main.o
GPIO.o
startup.o
main.c
GPIO.c
startup.c

## Slide 44: VPATH
Your project has many files in the different folders
VPATH variable specifies the list of directories that make should search for prerequisites and targets of rules
VPATH automatically search all Directory for Files 

## Slide 45: Pattern Rules
%.o : %.c
recipes….
 Tell how to make a .o file from a respectively .c file

## Slide 46: ‘notdir’ – not direct
Use to get file or folder without the direct/path

## Slide 47: Other Concept in Makefile

## Slide 48: Ifeq & export
Use many module in a test program  Modify Makefile with each module???  NO
We can use export

## Slide 49: Include Makefile
Include other makefile or file config of makefile
File make
File .mak
File .mk
Makefile
include <dir/file>